## Slide 1
UNICEF GIGA INITIATIVE — SCHOOL CLIMATE RISK PILOT
Tamil Nadu School
Flood Risk Analysis
Satellite-based hazard assessment using Sentinel-1 SAR
and Google Earth Engine
Google Earth Engine · Sentinel-1 SAR · Python · Folium
15
Schools analysed
2023
NE Monsoon season
3
Risk tiers assigned

## Slide 2
THE PROBLEM
Which schools are at risk —
and does flooding cut their connectivity?
🌊
Annual flooding
Tamil Nadu's northeast monsoon (Oct–Dec) causes recurring coastal floods affecting thousands of schools
📡
Connectivity at risk
Schools with no internet connectivity are doubly vulnerable — physical damage AND loss of digital learning
📊
No systematic data
No existing dataset links school locations, flood exposure, and connectivity status in one place
This analysis integrates Sentinel-1 satellite data with school location and connectivity records to answer these questions at school level.

## Slide 3
METHODOLOGY
Three-step pipeline — from satellite to risk score
01
Satellite data collection
Sentinel-1 SAR imagery — Oct to Dec 2023
Google Earth Engine processing
VV backscatter band (penetrates cloud cover)
Flood pixels: VV < -15 dB threshold
02
School exposure extraction
15 Tamil Nadu school locations loaded
1km buffer applied around each school
Flood pixel % extracted per buffer zone
Mean VV backscatter value per school
03
Risk scoring & mapping
HIGH risk: flood exposure ≥ 30%
MEDIUM risk: flood exposure 10–30%
LOW risk: flood exposure < 10%
Connectivity status overlaid on map

## Slide 4
KEY FINDINGS
School flood risk — Tamil Nadu northeast monsoon 2023
School
Connectivity
Flood exposure
Risk tier
School Puducherry Border
Connected
10.87%
MEDIUM
School Ramanathapuram
No connectivity
1.59%
LOW
Govt School Cuddalore
No connectivity
1.56%
LOW
Panchayat School Nagapattinam
No connectivity
1.07%
LOW
Govt School Madurai
Connected
0.95%
LOW
Govt High School Chennai
Connected
0.00%
LOW
High School Coimbatore
Connected
0.00%
LOW
⚠ Coastal schools (Cuddalore, Nagapattinam, Ramanathapuram) combine flood exposure WITH no connectivity — highest priority for resilience planning.

## Slide 5
RECOMMENDATIONS & NEXT STEPS
Recommendations
1
Prioritise Cuddalore, Nagapattinam, and Ramanathapuram schools for connectivity resilience investment — flood-exposed AND unconnected
2
Establish real-time monitoring for coastal schools using Sentinel-1 during northeast monsoon season (Oct–Dec)
3
Integrate this risk layer with UNICEF country office disaster preparedness planning